## Slide 1
XXXXX
008-00001-201
-
NONE
PARTS LIST, ADAPTER,
FIERO GT ALDL 160 BAUD,
V1.6.0,
ADAFRUIT TRINKET M0
P. ROMSKY
01 AUG 2022
P. ROMSKY
01 AUG 2022
P. ROMSKY
01 AUG 2022
008-00001-101
A1
-
-
INITIAL RELEASE
01 AUG 2022
PAR
PARTS LIST
MANUFACTURER SUPPLIER PRICE (USD)
REF --------------------------------- ---------------------------------- -------------
ITEM DESG NAME PART NUMBER NAME PART NUMBER QTY UM UNIT TOTAL DESCRIPTION
---- ------ ------------- ------------------- ------------ --------------------- --- --- ------ ------ -------------------------------------------------------------------------------------
1 A1 BUD INDUSTRY CU-789 DIGIKEY 377-1938-ND 1 EA $4.10 $4.10 BOX, ABS, 3.047 L x 2.047 x X 0.9 H INCHES, BLACK, WITH COVER AND HARDWARE
2 P1,W1 <PROPRIETARY> <PROPRIETARY> RED DEVIL GM-ALDL-12-BARE 1 EA $7.00 $7.00 CONNECTOR/CABLE, GM ALDL, 12 PIN, MALE, FULLY WIRED, BARE
RIVER
3 P2,W2 ASSMANN AK67321-1 DIGIKEY AE10417-ND 1 EA $4.44 $4.44 CABLE, USB 2, TYPE A MALE TO TYPE A MICRO MALE, 1 METER, DATA/POWER, SHIELDED, BLACK
4 A1A1 ADAFRUIT 3500 DIGIKEY 1528-2361-ND 1 EA $8.95 $8.95 BOARD, MICROCONTROLLER, ADAFRUIT TRINKET M0, ATSAMD21E18, 3.3V
5 A1A2 DFROBOT FIT0099 DIGIKEY 1738-1000-ND 1 EA $1.50 $1.50 PROTOBOARD, 3.08 L x 2.28 W INCHES, 100 MIL GRID, PLATED THROUGH HOLE, MATRIX PATTERN
6 A1TJ1 CINCH/JOHNSON 108-0902-001 DIGIKEY J151-ND 1 EA $1.19 $1.19 JACK, TEST, FEMALE, BANANNA, STANDARD, RED
7 A1F1 LITTLEFUSE 0297020.WXNV DIGIKEY F993-ND 1 EA $0.29 $0.29 FUSE, MINI BLADE, ATO, 20A, 32V
8 F1 LITTLEFUSE 0297002.WXNV DIGIKEY F986-ND 1 EA $0.29 $0.29 FUSE, MINI BLADE, ATO, 2A, 32V
9 Q1 ST MICRO BD239C DIGIKEY 497-12138-ND 1 EA $0.56 $0.56 TRANSISTOR, NPN, GENERAL PURPOSE, IC=2A, VCE=100V
10 CR1, NEXPERIA NZX3V3A,133 DIGIKEY 1727-4743-1-ND 2 EA $0.22 $0.44 DIODE, ZENER, 3.2V, 500mA, AXIAL
CR2
11 R1,R2 TE CONNECTIVE CFR16J1K0 DIGIKEY A104669CT-ND 2 EA $0.10 $0.20 RESISTOR, 1K OHM, 0.25W, 5%, AXIAL
12 R3 TE CONNECTIVE CFR16J270R DIGIKEY A129435CT-ND 1 EA $0.10 $0.10 RESISTOR, 260 OHM, 0.25W, 5%, AXIAL
13 ADAM TECH PH1-10-UA DIGIKEY 2057-PH1-10-UA-ND 1 EA $0.18 $0.18 PIN, HEADER, MALE, STRIP, 0.100 INCH PITCH, 10 PIN
14 STAPLES 604 STAPLES 604 1 SH $7.99 $0.02 PAPER, PRINTER, 8.5 x 11 INCH, A1 SIZE, 500 SHEET REAM
15 <ANY> <ANY> <ANY> <ANY> 1 AR $0.05 $0.05 INK, FOR PAPER, COMPATIABLE WITH PRINTER USED
16 TE CONNECTIVE 55PC0111-22-9 DIGIKEY A132397-01-ND 0 FT $0.62 $0.00 USE WIRES ENDS FROM W1 [WIRE, 22 AWG, Cu, STRANDED, ETFE JACKET, WHITE, 1 FOOT]
17 TENSILITY 30-02104 DIGIKEY 839-30-02104-1-ND 1 M $1.19 $1.19 WIRE, 26 AWG, Cu, SOLID, mPPE JACKET, WHITE, 1 METER
18 TE CONNECTIVE 55A0111-16-9 DIGIKEY A132383-01-ND 1 FT $1.05 $1.05 WIRE, 16 AWG, Cu, STRANDED, PVC JACKET, WHITE, 1 FOOT
19 ARROW MG24-4 HOME DEPOT SKU: 1003112860 1 SK $5.47 $0.23 GLUE, HOT, STICK, FOR STANDARD GLUE GUN, 24 STICK PACK
20 CHIP QUICK RASWLF.020 1OZ DIGIKEY RASWLF.0201OZ-ND 2 G $7.48 $0.53 SOLDER, ROSIN CORE, 24 AWG, Sn 96.5%/Ag 3%, 1 OZ
21 XYAXIS 008-00001-101 PAUL ROMSKY 008-00001-101 1 REF $0.00 $0.00 ASSEMBLY, ADAPTER, FIERO GT ALDL 160 BAUD, ADAFRUIT TRINEKT M0
22 XYAXIS 008-00001-201 PAUL ROMSKY 008-00001-201 1 REF $0.00 $0.00 PARTS LIST, ADAPTER, FIERO GT ALDL 160 BAUD, ADAFRUIT TRINEKT M0 (THIS DOCUMENT)
23 XYAXIS 008-00001-301 PAUL ROMSKY 008-00001-301 1 REF $0.00 $0.00 SCHEMATIC, ADAPTER, FIERO GT ALDL 160 BAUD, ADAFRUIT TRINEKT M0
24 XYAXIS 008-00001-901 PAUL ROMSKY 008-00001-901 1 SW $0.00 $0.00 SOFTWARE, SOURCE CODE, C/C++, ARDUINO IDE, FIERO GT ALDL ADAPTER, ADAFRUIT TRINEKT M0
-------
GRAND TOTAL $32.31 (USD)
UNITS OF MESURE (UM):
AR = AS REQUIRED
CUT = CUT
EA = EACH
FT = FOOT
G = GRAM
IN = INCH
M = METER
OZ = OUNCE
PC = PIECES
PK = PACK
REF = REFERENCE
RL = ROLL
SH = SHEET
SK = STICK
SP = SPOOL
SW = SOFTWARE
USD = UNITED STATES DOLLAR
**
** DENOTES: PREFIX REFERENCE DESIGNATORS WITH A1A2