## Slide 1
XXXXX
008-00001-301
-
NONE
SCHEMATIC, ADAPTER,
FIERO GT ALDL 160 BAUD,
V1.6.0,
ADAFRUIT TRINKET M0
P. ROMSKY
01 AUG 2022
P. ROMSKY
01 AUG 2022
P. ROMSKY
01 AUG 2022
-
-
INITIAL RELEASE
01 AUG 2022
PAR
NOTES
CONTENTS
SHEET FUNCTION
1 NOTES
MICROCONTROLLER
TWISTED PAIRS/TRIOS ARE INDICATED WITH THE SYMBOL. NO TWISTED PAIRS/TRIOS ARE IN THIS DESIGN.
1
THIS DRAWING IS AN ELECTRICAL SCHEMATIC NOT A WIRING DIAGRAM. THE CONNECTIONS REPRESENT ELECTRICAL
CIRCUITRY, NOT ACTUAL WIRING. HOWEVER, SOME WIRING SCHEMES CAN BE INFERRED FROM THIS DRAWING.
SIGNAL FLOW ARROWS SHOW THE PATH FROM SOURCE TO LOAD AND NOT NECESSARILY CURRENT FLOW.
SIGNALS IDENTIFIED AS ‘NC’ ARE NO CONNECTS AND ARE NOT TIED TOGETHER ELECTRICALLY.
CONNECTIONS ARE MADE WITH PINS SOLDERED ON THE A2 ASSEMBLY WHICH ARE THEN SOLDERED INTO THE A1 ASSEMBLY.
OTHER A1 CONNECTORS/PINS NOT SHOWN ARE NO CONNECT (NC).
PREFIX ALL REFERENCE DESIGNATORS WITH NEXT HIGHER ASSEMBLY.
WIRE COLORS ARE SUBJECT TO CHANGE.
5
6
2
3
4
7
SEE SEPARTE PARTS LIST
008-00001-101
A1
8

## Slide 2
MICROCONTROLLER
XXXXX
008-00001-301
-
NONE
-
-
INITIAL RELEASE
01 AUG 2022
PAR
A2 (PROTOBOARD)
A1
ADAFRUIT TRINKET M0
1
2
3
4
W2
USB 2
CABLE
TO
IBM PC
USB PORT
NC (+5V)
NC (+3.3V)
4
5
6
P2
PROGRAM WITH THE FILE:
Fiero_GT_ALDL_Adapter_V1_6_0.ino
USB TYPE A
(MALE)
160 Baud
PWM
Bit Data
9600 Baud
8 Bits
No Parity
1 Stop
1
2
3
4
J1
BAT
USB
GND
3V
U1
RESET
DOTSTAR
3-COLOR
LED
ATSAMD21E18
1
2
3
4
F
ON LED (GRN)
LED (RED)
M
P3
0
R1
1KΩ
0.25W
5%
1
2
CR1
3.3V
500mA
ALDL_160_3P3V
ALDL_160_BAUD
SES
R2
1KΩ
0.25W
5%
CR2
3.3V
500mA
2
SES_3P3V
Error Code
Pulses
GND
1
2
1
2
ECM_DIAG_REQ
DAIG_MODE
C
E
Q1
BD239C
2A
2W
Analog
DC
R3
260Ω
0.25W
5%
1
2
1
2
B
FIERO
ALDL
MATING
CONNECTOR
ON VEHICLE
FEMALE
ALDL
CONNECTOR
ON
ADAPTER
MALE
A
E
D
G
B
C
F
H
J
K
L
M
P1
TO
FIERO
ALDL
CONNECTOR
MALE
(BLK)
(WHT)
(YEL)
(RED)
(BLU)
NC
NC
NC
NC
NC
NC
NC
ECM_GROUND
ALDL_160_BAUD **
SES
FUEL_PUMP
ECM_DIAG_REQ ***
SHIFT_LIGHT
ANTI_LOCK_BRAKE_TEST
NC
INFLATE_RESTRAINT_TEST
NC
ALDL_8192_BAUD
TJ1
(RED)
REMOTE FUEL PUMP SWITCH
(+12V IN)
(16 AWG)
W1
ALDL
CABLE
1
2
~1
(16AWG)
F1
20A
FAST BLOW
1
2
F1
2A
FAST
BLOW
NC
NC
NC
3
4
RST
NC
A1 (BOX)
USB
TYPE A MICRO
(MALE)
8
Open to GND = 5.0V Pin ~1 ADC set to 0x000 = 0.000V
10KΩ to GND = 2.5V Pin ~1 ADC set to 0x800 = 1.650V
3.9KΩ to GND = 1.4V Pin ~1 ADC set to 0xB84 = 2.376V
Short to GND = 0.0V Pin ~1 ADC set to 0xFFF = 3.300V
TP1
TP1:
8mA
[MAX]
550uA
[TYP]
*** ECM_DIAG_REQ IS A HI-Z INPUT
ON THE ECM PULLED UP TO 10KΩ.
** ALDL_160_BAUD IS A 5V TO GND
DIGITAL PWM SIGNAL FROM THE ECM.
3.3V
[MAX]
5V [TYP]
32V [MAX]
8.6mA
[TYP]